## Slide 1: Low Pass Filter Design Example & Simulation

## Slide 2
Election
Treasury Duty Relief & Appointment
Any other business

## Slide 4
Example LPF Design
Clean up a second harmonic at least 17dB below Fc
Freg = 7 Mhz and use a Butterworth filter. Shunt Type.
Impedance= 50 Ohm in and 50 Ohm out.
Fc= 7 Mhz
Fs= 14 Mhz
Normalised Freg. = F/Fc = 2.0
Check Table for Frequency Response.
It shows N=4
Check table with normalized L & C values

## Slide 7
Example
Check table with normalized L & C values
C1= 0.7654 L2=1.8478
C3=1.8478 L4=0.7654

## Slide 8
2.1µH
C
Farad
Same Process:
C3= 840pF L4= 870nH or 0.87µH
Example work out
50 Ohm
50 Ohm
348p
840p
2.1uH
0.87uH

## Slide 9
Things to Consider
50 Ohm
50 Ohm
348p
840p
2.1uH
0.87uH
Insertion loss and Amplification
Standard Values versus Calc values
Coil Type.
Do you like a high or low Q
C suitability for the target Frequency
C max Voltage
L max Current or Power Rating
L and T dependence.
Keep in mind tolerances of C & L
Rp for C
Rs for L
Humidity impact
T impact on permanent change of C
G forces impact / Mechanical Structure
Ultimate Rejection

## Slide 10
Too much attenuation 5th order LPF
Example of 1680kHz Low Power Transmitter ( 10mW).
Left no filter / Right after filter .

## Slide 11
Before and After . Improved matching but still too much attenuation 5th order LPF
Output becomes micro watt QRP levels.

## Slide 12
Before and After . Improved matching but still too much attenuation 5th order LPF

## Slide 13
Sources and References:
ARRL 2006 Handbook

## Slide 14
NOW SIMULATION
Tina Simulator
TI Student Version